## Slide 1
DISCOVER . LEARN . EMPOWER
Lecture - 3
Data Representation
APEX INSTITUTE OF TECHNOLOGY
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
Computer Organization & Architecture (21CSH-281)
Faculty: Mr. Siddharth Kumar (E12853)

## Slide 2: COA: Course Objectives
1. The purpose of the course is to introduce principles of computer organization and the basic architectural concepts.
2. It begins with basic organization, design, and programming of a simple digital computer and introduces simple register transfer language to specify various computer operations.
3. Topics include computer arithmetic, instruction set design, microprogrammed control unit, pipelining and vector processing, memory organization and I/O systems, and multiprocessors.
4. To familiarize Students with the detailed Architectures of a Central Processing Unit.
5. Learn the different types of serial communication techniques.

## Slide 3: COURSE OUTCOMES
On completion of this course, the students shall be able to:-
CO1 | Identify and interpret the basics of instruction sets and their impact on the design, organization, and functionality of various functional units of a computer comparable to the CPU, memory organization, I/O organization, and parallel processors.

## Slide 4: Unit-1 Syllabus
Unit-1 | Basic Organization of Computer | Contact Hours:15 hours
Data representation | Signed number representation, fixed and floating-point representations, character representation. | 
Functional blocks of a computer | CPU, memory, input-output subsystems, control unit. | 
Instruction set architecture of a CPU: | Registers, instruction execution cycle, RTL interpretation of instructions, addressing modes, instruction set. Outlining instruction sets of some common CPUs. | 
Computer arithmetic | Integer addition and subtraction, ripple carry adder, carry look-ahead adder, etc. multiplication – shift-and-add, Booth multiplier, carry save multiplier, etc. Division restoring and non-restoring techniques, floating point arithmetic, IEEE 754 format. | 

## Slide 5: SUGGESTIVE READINGS
Text Books / Reference Books
TEXT BOOKS
T1: Computer System Architecture M. M. Mano: 3rd ed., Prentice Hall of India, New Delhi, 1993.
T2: Computer Organization and Design: The Hardware/Software Interface, David A. Patterson and John L. Hennessy.
T3: Computer Organization and Embedded Systems, Carl Hamacher.
REFERENCE BOOKS
R1: Computer Architecture and Organization, John P. Hayes.
R2: Computer Organization and Architecture: Designing for Performance, William Stallings.
R3: Computer System Design and Architecture, Vincent P. Heuring and Harry F. Jordan.

## Slide 6: Contents to be Covered
Number System
Conversion From Binary to Decimal
Conversion From Decimal to Binary
Signed Numbers
Unsigned and Signed Numbers

## Slide 7: Number System
Data Representation
  Decimal
  Binary
  Octal
  Hexadecimal

## Slide 8: Number System
Complements
  (r-1)’s complement
    9’ complement
    1’ complement
  (r’)s complement
    10’ complement
    2’ complement

## Slide 9: Conversion between Representations
Now we can represent a quantity in different number representations
  How can we convert a decimal number to binary?
  How can we then convert a binary number to a decimal one?

## Slide 10: Conversion From Binary to Decimal
Converting from binary to decimal. This conversion is based on the formula:
d = dn-12n-1 + dn-22n-2 +…+ d222 + d121 + d020
while remembering that the digits in the binary representation are the coefficients.
For example, given 101011two, in decimal, it is
25 + 23 + 21 + 20 = 43.

## Slide 11: Conversion From Decimal to Binary
Converting from decimal to binary:
  Repeatedly divide it by 2, until the quotient is 0.
  Write down the remainder, the last remainder first.
Example: 11ten is 1011two
Quotient | Remainder
5 | 1
2 | 1
1 | 0
0 | 1

## Slide 12: Conversion From Decimal to Binary
Why can a binary number be obtained by keeping on dividing it by 2, and why should the last remainder be the first bit?
  The decimal number can be represented by the summation of the powers of 2:
  d = dn-12n-1 + dn-22n-2 +…+ d222 + d121 + d020
    For example, 19 = 16 + 2 + 1 = 1 * 24 + 0 * 23 + 0 * 22 + 1 * 21 + 1 * 20.
  The binary representation is the binary coefficients.
    So 19ten in binary is 10011two.
  So the conversion is to find the coefficients. Easiest way to do so is to repeatedly divide it by 2.
    For example, 19 = 1 * 101 + 9 * 100. How do you get the 1 and 9? You divide 19 by 10 repeatedly until the quotient is 0, same as binary!

## Slide 13: Conversion between Base 16 and Base 2
Extremely easy.
  From base 2 to base 16: divide the digits in to groups of 4, then apply the table.
  From base 16 to base 2: replace every digit by a 4-bit string according to the table.
Because 16 is 2 to the power of 4.

## Slide 14: Addition in binary
39ten + 57ten = ?
How to do it in binary?

## Slide 15: Addition in binary
The addition is bit by bit.
We will encounter at most 4 cases, where the leading bit of the result is the carry:
  0+0+0=00
  1+0+0=01
  1+1+0=10
  1+1+1=11

## Slide 16: Addition in Binary
First, convert the numbers to binary forms. We are using 8 bits.
  39ten -> 001001112
  57ten -> 001110012
Second, add them.
  00100111
  00111001
  01100000

## Slide 17: Subtraction in Binary
57ten – 39ten = ?

## Slide 18: Subtraction in binary
Do this digit by digit.
No problem if
  0 - 0 = 0,
  1 - 0 = 1
  1 – 1 = 0.
When encounter 0 - 1, set the result to be 1 first, then borrow 1 from the next more significant bit, just as in decimal.
  Borrow means setting the borrowed bit to be 0 and the bits from the bit following the borrowed bit to the bit before the current bit to be 1.
  Think about, for example, subtracting 349 from 5003 (both based 10). The last digit is first set to be 4, and you will be basically subtracting 34 from 499 from now on.

## Slide 19: Subtraction in Binary
  00111001
  00100111
  00010010

## Slide 20: Signed Numbers
Two’s complement in n bits:
  The negative of a two’s complement is given by inverting each bit (0 to 1 or 1 to 0) and then adding 1, ignore any carry beyond n bits (take only the lower n bits).
If numbers are represented in n bits:
  the positive numbers are from 0000…01 to 0111…11,
  0 is all 0: 0000…00,
  the negative numbers are from 1000…00 to 1111…11.
The leading bit is called the “sign bit”: 0 means non-negative, 1 means nagative

## Slide 21: Signed numbers
What is (-57ten) in binary in 8 bits?
  00111001 (57ten in binary)
  11000110 (invert)
  11000111 (add 1)

## Slide 22: Two’s Complement Representation
Type (C) | Number of bits | Range (decimal)
char | 8 | -128 to 127
short | 16 | -32768 to 32767
int | 32 | -2,147,483,648 to 2,147,483,647
long long | 64 | -9,223,372,036,854,775,808 to 9,223,372,036,854,775,807
n+1 bits (in general) | n+1 | -2n to 2n - 1

## Slide 23: Why use 2’s complement? (Not required)
If you think about it, x in 2’s complement with n bits is just 2n-x.
Consider 01101 +(– 00011) = 01101 – 00011 = 01010 (13-3=10 in decimal).
01101 – 00011 = 01101 + 100000 – 00011 – 100000
= 01101 + (100000 – 00011) – 100000
= 01101 + 11101 – 100000
= 101010 – 100000
= 01010
11101 is the 2’s complement of 00011.
Means that computer (the adder) does not have to be specifically redesigned for dealing with negative numbers, make life easier for the computer
The reason is, assume you are subtracting a with b , where 2^{n-1}>a>b>0. Note that a-b=a+2^{n}-b-2^{n}. But 2^{n}-b is the 2’s complement of b. So if represented in binary forms, a+2^{n}-b will be having a 1 bit in bit n and some thing in bit 0 to bit n-2 equal to a-b. Bit n-1 will be 0. So you take what is in bit 0 to bit n and it must be a-b.

## Slide 24: Subtraction with 2’s Complement
How about 39ten + (-57ten)?

## Slide 25: Subtraction with 2’s Complement
First, what is (-57ten) in binary in 8 bits?
  00111001 (57ten in binary)
  11000110 (invert)
  11000111 (add 1)
Second, add them.
  00100111
  11000111
  11101110

## Slide 26: Converting 2’s complement to decimal
  What is 11101110ten in decimal if it represents a two’s complement number?
  11101110 (original)
  11101101 (after minus 1)
  00010010 (after inversion)

## Slide 27: Two’s Complement Representation
Sign extension
  We often need to convert a number in n bits to a number represented with more than n bits
    From char to int for example
  This can be done by taking the most significant bit from the shorter one and replicating it to fill the new bits of the longer one
    Existing bits are simply copied

## Slide 28: Sign Extension Example
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  | -3ten -3ten -3ten
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 |  | 
- How about unsigned numbers?

## Slide 29: Sign Extension Example: Unsigned
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  | 252ten 252ten 252ten
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  | 

## Slide 30: Unsigned and Signed Numbers
Note that bit patterns themselves do not have inherent meaning
  We also need to know the type of the bit patterns
  For example, which of the following binary numbers is larger?

## Slide 31: Unsigned and Signed Numbers
Note that bit patterns themselves do not have inherent meaning
  We also need to know the type of the bit patterns
  For example, which one is larger?
    Unsigned numbers?
    Signed numbers?

## Slide 32: Fixed-Point Representation
This representation has fixed number of bits for integer part and for fractional part.
For example, if given fixed-point representation is IIII.FFFF, then you can store minimum value is 0000.0001 and maximum value is 9999.9999.
There are three parts of a fixed-point number representation: the sign field, integer field, and fractional field.

## Slide 33
We can represent these numbers using:
Signed representation: range from -(2(k-1)-1) to (2(k-1)-1), for k bits.
1’s complement representation: range from -(2(k-1)-1) to (2(k-1)-1), for k bits.
2’s complementation representation: range from -(2(k-1)) to (2(k-1)-1), for k bits.
2’s complementation representation is preferred in computer system because of unambiguous property and easier for arithmetic operations.

## Slide 34: Floating-Point Representation
This representation does not reserve a specific number of bits for the integer part or the fractional part.
Instead it reserves a certain number of bits for the number (called the mantissa or significand) and a certain number of bits to say where within that number the decimal place sits (called the exponent).
The floating number representation of a number has two part: the first part represents a signed fixed point number called mantissa.
The second part of designates the position of the decimal (or binary) point and is called the exponent.
The fixed point mantissa may be fraction or an integer. Floating -point is always interpreted to represent a number in the following form: Mxre.

## Slide 35
Only the mantissa m and the exponent e are physically represented in the register (including their sign). A floating-point binary number is represented in a similar manner except that is uses base 2 for the exponent.
A floating-point number is said to be normalized if the most significant digit of the mantissa is 1.
So, actual number is (-1)s(1+m)x2(e-Bias), where s is the sign bit, m is the mantissa, e is the exponent value, and Bias is the bias number.
Note that signed integers and exponent are represented by either sign representation, or one’s complement representation, or two’s complement representation.

## Slide 36: Key points
Number System
Conversion of one number system to another
Unsigned and Signed Numbers

## Slide 37: Character Representation
Character sets
  Standard ASCII: 7-bit character codes (0 – 127)
  Extended ASCII: 8-bit character codes (0 – 255)
  Unicode: 16-bit character codes (0 – 65,535)
  Unicode standard represents a universal character set
    Defines codes for characters used in all major languages
    Used in Windows-XP: each character is encoded as 16 bits
  UTF-8: variable-length encoding used in HTML
    Encodes all Unicode characters
    Uses 1 byte for ASCII, but multiple bytes for other characters
Null-terminated String
  Array of characters followed by a NULL character

## Slide 38: ASCII (American Standard Code for Information Interchange) Codes
Examples:
  ASCII code for space character = 20 (hex) = 32 (decimal)
  ASCII code for ‘A' = 41 (hex) = 65 (decimal)
  ASCII code for 'a' = 61 (hex) = 97 (decimal)

## Slide 39: Control Characters
The first 32 characters of ASCII table are used for control
Control character codes = 00 to 1F (hex)
Examples of Control Characters
  Character 0 is the NULL character  used to terminate a string
  Character 9 is the Horizontal Tab (HT) character
  Character 0A (hex) = 10 (decimal) is the Line Feed (LF)
  Character 0D (hex) = 13 (decimal) is the Carriage Return (CR)
  The LF and CR characters are used together
    They advance the cursor to the beginning of next line
One control character appears at end of ASCII table
  Character 7F (hex) is the Delete (DEL) character

## Slide 40: References
Text Books:
  Computer System Architecture M. M. Mano:, 3rd ed., Prentice Hall of India, New Delhi, 1993.
  Computer Organization and Design: The Hardware/Software Interface, David A. Patterson and John L. Hennessy.
  Computer Organization and Embedded Systems, Carl Hamacher.

## Slide 41
THANK YOU
For queries
Email: siddharth.e12853@cumail.in